## Slide 1: Computer Architectures Session 3
Pipelined RISC-V processor with control-hazard handling
&
Advanced acceleration
TAs :
  Xiaoling Yi (xiaoling.yi@kuleuven.be)
  Chao Fang (chao.fang@kuleuve.be)
  Adrian Kneip (adrian.kneip@kuleuve.be)

## Slide 2: Timeline
Session 1
Session 2
Session 3
Simulation
Functional single cycle processor
Single cycle processor with multiplication
Pipelined processor
Data hazard resolution
Advanced acceleration
Project Feedback
[Mar-04/05]
[Apr-01/02]
[Apr-23/24]
Session 4
[May-11/13]
Written Exam Exercises
Submission Deadline [May-1]
Backend flow (synthesis-only)
Control hazard resolution

## Slide 3: Last session recap
Single cycle processor skeleton
Functional single cycle processor
Single cycle processor with multiplication
Pipelined processor
Pipelined processor with data hazard resolution
Advanced acceleration
Simulation
Backend flow (synthesis-only)
Backend flow (complete)
Session 1
Session 2
Session 3
[Apr-01/02]

## Slide 4: Last session recap
Pipelined Processor
Mult2
Mult3
Backend complete
Prerequisite for this session!

## Slide 5: Today’s session: Advanced acceleration
Single cycle processor skeleton
Functional single cycle processor
Single cycle processor with multiplication
Pipelined processor
Pipelined processor with data hazard resolution
Advanced acceleration
Simulation
Backend flow (synthesis-only)
Backend flow (complete)
Session 1
Session 2
Session 3
[Apr-23/24]
Obj-1: mult4

## Slide 6: Obj-1: mult4
Matrix-matrix multiplication (MULT4)
  Input matrices stored in mult4_dmem_content.txt
  Methods
  Add more RTL modules
  Modify the mult4_imem program
  or both …
  Pass the simulation
  Synthesize
0x1
0x2
0x3
…
0x15
0x16
0x17
…
0x163
0x1AE
0x1F9
…
Data memory layout:
W[K][C]
(given)
I[B][C]
(given)
O[B][K]
(expected)
Testing example:
I[B][C]
W[C][K]
O[B][K]
(B = 4 , C = 5, K = 6)
[Addr/8]
0
19
20
49
50
73
Row-major
Column-major
Row-major
We check on this part!
Results are written back to this part of the data memory
Notes: [Jun-0324]:
+ dmem addr index
+ dmem data layout

## Slide 7
MULT4: our baseline solution
RISC-V assembly code
C code:
I[B][C]
W[C][K]
O[B][K]
Required modifications to the processor
Full data forwarding logic
Hazard detection unit (control/data hazard)
Testing example:
I[B][C]
W[C][K]
O[B][K]
(B = 4 , C = 5, K = 6)
addi x25, x0, 0 # input's address starting point in dmem addi x26, x0, 160 # weight's address starting point in dmem addi x27, x0, 600 # output's address starting point in dmem addi x11, x0, 5 # total C loop size addi x12, x0, 6 # total K loop size addi x13, x0, 4 # total B loop size addi x21, x0, 0 # C loop index starts with 0 addi x22, x0, 0 # K loop index starts with 0 addi x23, x0, 0 # B loop index starts with 0 addi x7, x0, 0 # accumulation result initialization B_CHECK: beq x23, x13, B_END K_CHECK: beq x22, x12, K_END C_CHECK: beq x21, x11, C_END ld x4, 0(x25) # load 1 input data ld x5, 0(x26) # load 1 weight data mul x6, x4, x5 # multiply the input with the weight add x7, x7, x6 # accumulate the result addi x21, x21, 1 # C loop index +1 addi x25, x25, 8 # input's 64-bit word address +1 addi x26, x26, 8 # weight's 64-bit word address +1 jal C_CHECK C_END: addi x21, x0, 0 # C loop index restarts with 0 sd x7, 0(x27) # store the output data addi x7, x0, 0 # accumulation result reset to 0 addi x22, x22, 1 # K loop index +1 addi x25, x25, -40 # input's 64-bit word address -5 addi x27, x27, 8 # output's 64-bit word address +1 jal K_CHECK K_END: addi x22, x0, 0 # K loop index restarts with 0 addi x23, x23, 1 # B loop index +1 addi x25, x25, 40 # input's 64-bit word address +5 addi x26, x26, -240 # input's 64-bit word address -30 jal B_CHECK B_END:
Notes: [Jun-0324]:
+ diagram
+ todo list

## Slide 8: I. Full data forwarding logic (Book §4.7)
addi x25, x0, 0 # input's address starting point in dmem addi x26, x0, 160 # weight's address starting point in dmem addi x27, x0, 600 # output's address starting point in dmem addi x11, x0, 5 # total C loop size addi x12, x0, 6 # total K loop size addi x13, x0, 4 # total B loop size addi x21, x0, 0 # C loop index starts with 0 addi x22, x0, 0 # K loop index starts with 0 addi x23, x0, 0 # B loop index starts with 0 addi x7, x0, 0 # accumulation result initialization B_CHECK: beq x23, x13, B_END K_CHECK: beq x22, x12, K_END C_CHECK: beq x21, x11, C_END ld x4, 0(x25) # load 1 input data ld x5, 0(x26) # load 1 weight data mul x6, x4, x5 # multiply the input with the weight add x7, x7, x6 # accumulate the result addi x21, x21, 1 # C loop index +1 addi x25, x25, 8 # input's 64-bit word address +1 addi x26, x26, 8 # weight's 64-bit word address +1 jal C_CHECK C_END: addi x21, x0, 0 # C loop index restarts with 0 sd x7, 0(x27) # store the output data addi x7, x0, 0 # accumulation result reset to 0 addi x22, x22, 1 # K loop index +1 addi x25, x25, -40 # input's 64-bit word address -5 addi x27, x27, 8 # output's 64-bit word address +1 jal K_CHECK K_END: addi x22, x0, 0 # K loop index restarts with 0 addi x23, x23, 1 # B loop index +1 addi x25, x25, 40 # input's 64-bit word address +5 addi x26, x26, -240 # input's 64-bit word address -30 jal B_CHECK B_END:
MULT4:
Notes: [Jun-0324]: + slide order change

## Slide 9: I. Full data forwarding logic (Book §4.7)
MULT4:
Similar to the case in MULT3
Another data forwarding scenario
Beyond data forwarding
Can’t get data from the future.
We need to stall the “mul” instruction.
Notes: [Jun-0324]:
- replace “Forwarding already known results”
- delete the 2nd arrow: it was not covered/needed previously. Part of this session’s forwarding — the data forwarding after 1-cycle stall.
+ condition explanation

## Slide 10: II. Data hazard resolution with stalling
Patterson Book. FIGURE 4.56
Load and use
Notes: [Jun-0324]: + explanation

## Slide 11: II. Data hazard resolution with stalling
After 1-cycle stall, the hazard between [ld] and [and] becomes a normal WB->EX forwarding.
Load and use
Notes: [Jun-0324]: + explanation

## Slide 12
Prevent PC and IF/ID register updates if hazard is detected
Add bubble to control signal if stall
To be implemented:
Stall
WB->EX forwarding (register_file)
1.
2.
Patterson Book. FIGURE 4.58
II. Data hazard resolution with stalling

## Slide 13: II. Data hazard resolution with stalling
After 1-cycle stall, the hazard between [ld] and [and] becomes a normal WB->EX forwarding.
Load and use
Now we need the register file forwarding here after stalling.
Notes: [Jun-0324]: + explanation

## Slide 14: I. Full data forwarding logic (Book §4.7)
MULT4:
Register file data forwarding
Modify the register_file.v
Think:
In which case should you forward the wdata to rdata?
Notes: [Jun-0324]:
- replace “Forwarding already known results”
- delete the 2nd arrow: it was not covered/needed previously. Part of this session’s forwarding — the data forwarding after 1-cycle stall.
+ condition explanation

## Slide 15
addi x25, x0, 0 # input's address starting point in dmem addi x26, x0, 160 # weight's address starting point in dmem addi x27, x0, 600 # output's address starting point in dmem addi x11, x0, 5 # total C loop size addi x12, x0, 6 # total K loop size addi x13, x0, 4 # total B loop size addi x21, x0, 0 # C loop index starts with 0 addi x22, x0, 0 # K loop index starts with 0 addi x23, x0, 0 # B loop index starts with 0 addi x7, x0, 0 # accumulation result initialization B_CHECK: beq x23, x13, B_END K_CHECK: beq x22, x12, K_END C_CHECK: beq x21, x11, C_END ld x4, 0(x25) # load 1 input data ld x5, 0(x26) # load 1 weight data mul x6, x4, x5 # multiply the input with the weight add x7, x7, x6 # accumulate the result addi x21, x21, 1 # C loop index +1 addi x25, x25, 8 # input's 64-bit word address +1 addi x26, x26, 8 # weight's 64-bit word address +1 jal C_CHECK C_END: addi x21, x0, 0 # C loop index restarts with 0 sd x7, 0(x27) # store the output data addi x7, x0, 0 # accumulation result reset to 0 addi x22, x22, 1 # K loop index +1 addi x25, x25, -40 # input's 64-bit word address -5 addi x27, x27, 8 # output's 64-bit word address +1 jal K_CHECK K_END: addi x22, x0, 0 # K loop index restarts with 0 addi x23, x23, 1 # B loop index +1 addi x25, x25, 40 # input's 64-bit word address +5 addi x26, x26, -240 # input's 64-bit word address -30 jal B_CHECK B_END:
Control Hazard:
MULT4:
III. Control Hazard solution (Book §4.8)

## Slide 16
III. Control Hazard solution (Book §4.8)
We missed our Branch Unit!
  Not used in MULT2 & MULT3
  But will be useful here for
    BR instruction
    JAL instruction
  Which pipeline should we put it to?
    What is its input?
    How is the data computed?
    Who is using its output?
Branch Unit ?

## Slide 17
Recall §4.6:
We know if the branch was taken at the MEM stage.
Patterson Book. FIGURE 4.49
III. Control Hazard solution (Book §4.8)

## Slide 18
Branch was taken
These should be discarded
Such solution comes at a cost…
Recall §4.6:
By that time, 3 instructions are already in the pipeline.
They should be discarded, hence 3 cycles are wasted (§4.8.1).
III. Control Hazard solution (Book §4.8)

## Slide 19: Control Hazard - Our baseline
branch_unit (pc value)
Flush instruction if branch is taken (§4.8.2)
To save this overhead:
Make branch/jump decision ASAP (at the ID stage, §4.8.2).
This is our baseline architecture for MULT4 (in terms of saving the total cycle amount).
Patterson Book. FIGURE 4.62
branch
taken?
We still use the branch-not-taken prediction (in our baseline).
  ID judges the branch/jump.
  IF basically fetches imem[PC+4].
  If branch-taken/jump, next PC is overwritten and the false IF instruction is flushed before next clock edge comes.
Feel free to use different prediction scheme if you find it valuable(§4.8.3).

## Slide 20: IV. PLAN B – hazards can be solved with nop insertion
ld x4, 0(x25) # load 1 input data ld x5, 0(x26) # load 1 weight data nop mul x6, x4, x5 # multiply the input with the weight add x7, x7, x6 # accumulate the result addi x21, x21, 1 # C loop index +1 addi x25, x25, 8 # input's 64-bit word address +1 addi x26, x26, 8 # weight's 64-bit word address +1 jal C_CHECK nop nop nop C_END: addi x21, x0, 0 # C loop index restarts with 0 sd x7, 0(x27) # store the output data addi x7, x0, 0 # accumulation result reset to 0 addi x22, x22, 1 # K loop index +1 addi x25, x25, -40 # input's 64-bit word address -5 addi x27, x27, 8 # output's 64-bit word address +1 jal K_CHECK nop nop nop K_END: addi x22, x0, 0 # K loop index restarts with 0 addi x23, x23, 1 # B loop index +1 addi x25, x25, 40 # input's 64-bit word address +5 addi x26, x26, -240 # input's 64-bit word address -30 jal B_CHECK nop nop nop B_END:
addi x25, x0, 0 # input's address starting point in dmem addi x26, x0, 160 # weight's address starting point in dmem addi x27, x0, 600 # output's address starting point in dmem addi x11, x0, 5 # total C loop size addi x12, x0, 6 # total K loop size addi x13, x0, 4 # total B loop size addi x21, x0, 0 # C loop index starts with 0 addi x22, x0, 0 # K loop index starts with 0 addi x23, x0, 0 # B loop index starts with 0 addi x7, x0, 0 # accumulation result initialization B_CHECK: beq x23, x13, B_END nop nop nop K_CHECK: beq x22, x12, K_END nop nop nop C_CHECK: beq x21, x11, C_END nop nop nop
Understand the program, locate the hazard, understand your design, upgrade the imem…
Don’t just copy and paste this one!
Understand your architecture and insert the necessary nops.
Hazard control and nop insertion are related
  The better hazard control logic you have,
  The fewer nops you will need,
  The better performance you will achieve.
[Fail-Safe] If the deadline is right ahead,
at least make your processor functional on MULT4!
Recall MULT2, the software solution.

## Slide 21: IV. PLAN B – hazards can be solved with nop insertion
Whenever you change the program, DO NOT FORGET to regenerate the machine code (imem_content)!
Make use of the online tool we mentioned in session-1 (link-online-converter, link-github).
1. Paste your assembly code in Editor.
2. Go to Simulator and click the Green button.
3. Upgrade the imem_content (remove “0x”!).
4. Never forget to add the finishing lines. 👇

## Slide 22: Today’s session: task summary
With session_guide.pdf
Study the RUN CYCLE-ACCURATE SIMULATION and RUN BACKEND FLOW
Follow the TASKS TO BE DONE and fill in the report.docx
Copy-paste your finished /RTL/*.v into the SOLUTION folders.
Obj-1  RTL_SOLUTION5_pipeline_hazard_advanced_MULT4
Note:
We use universal test patterns for fair grading.
Do not modify cpu_tb.v & sky130_sram_2rw.v
Do not modify mult4_dmem_content.txt
This time you can modify mult4_imem_content.txt

## Slide 23
Useful resources to make it go faster!
  Patterson Book. End of section 4.8 on branch prediction tricks.
  Patterson Book. From Section 4.10 on advanced acceleration tricks.
  RISC-V specification. Chapter 17 on the “V” Standard Extension for Vector Operations
Be creative
Project handover
Deadline: 1st May
Grading | 
ITEM | Points
Functional pipelined MULT2 | 0.25
Functional pipelined MULT3 | 0.25
Functional MULT4 | 0.25
Advanced MULT4 #cycles <= baseline imp. (1636 cc) | 0.25
Report | 1.0
Total | 2.0